## Slide 1: Carry Lookahead Adder

## Slide 3
A3
B3
A2
B2
A1
B1
A0
B0
C2
C3
C1
C0
Cin
Cin
Cout
A
B
S
S3
Cin
Cout
A
B
S
S2
Cin
Cout
A
B
S
S1
Cin
Cout
A
B
S
S0

## Slide 4
0
0
1
1
0
1
1
1
1
0
1
1
0
Compute 0101b + 0111b
Cin
Cout
A
B
S
S3
Cin
Cout
A
B
S
S2
Cin
Cout
A
B
S
S1
Cin
Cout
A
B
S
S0

## Slide 5
Adder 3
Adder 2
Adder 1
Adder 0
0
0
1
1
0
1
1
1
0
I don’t want to wait! Looks like Adder2 can have its carry figured out immediately!

## Slide 6
Adder 3
Adder 2
Adder 1
Adder 0
0
0
1
1
0
1
1
1
0
Sure, Adder3, I have both inputs as 1, so I will carry 1 for you no matter what Adder 1 says. BTW, Adder 1, what is your carry?

## Slide 7
Adder 3
Adder 2
Adder 1
Adder 0
0
0
1
1
0
1
1
1
0
Adder2, don’t look at me, ask Adder0 instead. I’m adding 0 and 1, so I’ll carry whatever Adder 0 carries.

## Slide 8: What does that imply?
“Sure, Adder3, I have both inputs as 1, so I will carry 1 for you no matter what Adder 1 says.”
An adder can generate carry if both its input are 1s. This property cuts the long-chained carry dependency into pieces.
We call it a “Generate” signal. G in short.
G = A and B

## Slide 9: What does that imply?
- “Adder2, don’t look at me, ask Adder0 instead. I’m adding 0 and 1, so I’ll carry whatever Adder 0 carries.”
If an adder is adding a 0 and a 1, its Cout will be exactly same as its Cin. We can directly connect its Cin signal directly to its Cout in this case, so that the adder becomes transparent (eliminated) in the dependency chain.
We call this a “Propagate” signal. P in short.
P = A xor B

## Slide 10
A=B=0
P = 0
G = 0

## Slide 11
A=B=1
P = 0
G = 1

## Slide 12
A != B
P = 1
G = 0

## Slide 13: P & G
PG | Meaning
00 | Adder sees 0 + 0 + Cin, knows Cout = 0 for sure.
01 | Adders sees 1 + 1 + Cin, knows Cout = 1 for sure.
10 | Propagate Cin to Cout. G becomes don’t care.
11 | ------------------------------------------------------------ Unreachable because A & B, A xor B can’t be both 1
Generate, cuts propagation
Propagate, transparent in propagation

## Slide 14: Recursive formula for carry
Consider bit i in a N bit adder.
Your carry =
=
If you keep substitute with , you eventually reach a formula where is some function of and and , which is equal to
You are “looking ahead” all the carries, finding your way through all units that are “propagating”, until you find someone that’s “generating” or you reach original
All adders no longer have to wait for signal propagation delay because all P & Gs are computed in parallel and made available to all adders by a Lookahead logic circuit.

## Slide 15: Example
=

## Slide 17
Assume all combinational logic (Propagate, Generate, Sum and Carry) take same amount of time dt (for simplicity, not in reality!)
Every dt, new produced values are marked red, done adders are marked with green circle

## Slide 18
0
0
1
0
0
1
1
1
0
0
T=0
Carry Lookahead Unit

## Slide 19
0
0
1
0
0
1
1
1
0
0
0
1
0
Propagate
Propagate
1
0
T=1
P=0
G=1
P=1
G=0
P=1
G=0
P=0
G=0

## Slide 20
0
0
1
0
0
1
1
1
0
0
0
1
0
Propagate
1
Propagate
1
1
0
0
1
0
0
1
T=2
P=0
G=1
P=1
G=0
P=1
G=0
P=0
G=0

## Slide 21
0
0
1
0
0
1
1
1
0
0
0
1
0
1
0
0
1
0
0
1
1
0
T=3
P=0
G=1
P=1
G=0
P=1
G=0
P=0
G=0
Propagate
1
Propagate
1

## Slide 22
0
0
1
0
0
1
1
1
0
0
0
1
0
1
0
0
1
0
0
1
1
0
1
0
T=4
P=0
G=1
P=1
G=0
P=1
G=0
P=0
G=0
Propagate
1
Propagate
1

## Slide 23: 4-bit Carry Lookahead Unit at a glance
To achieve better performance, we often need to sacrifice area and energy. This is an engineering trade-off

## Slide 26: Implementation of CLA
Assuming Mux does not have any delays

## Slide 27: Implementation of CLA
Essentially a Fan-in series of 4 4-input Mux

## Slide 28: What if Mux has delay?
This implementation still causes propagation trouble

## Slide 29: Solution
Combine fan in series into a big mux
This circuit behaves exactly same as the “Carrylookahead Unit”. However, no hardware engineer will code 2^8 input mux. In fact, a lot of inputs in those big muxes are duplicates and/or don’t-cares. We can simplify the carry-MUX function into much more concise circuits with P&G signals using the recursive formula.